## Slide 1: Accelerated Design of Silicon Photonic Devices with Neural Networks
Randi Wan
Jonathan Levine
Jacob Ryall
Deng Mading
Prof. Leonard MacEachern
Prof. Winnie Ye

## Slide 2: Main Motivations and Goals
SOI grating couplers are used to couple light into and out of photonic circuits
They are highly sensitive to their physical parameters
Simulated using FDTD simulations which require significant computational resources
Licensing is very expensive (order of 10k/ year)
Accelerate the design silicon photonic components with artificial neural networks
We chose SOI grating couplers because they are one of the most important devices in the SOI platform and they offer a straightforward proof of concept (are only characterized by a couple parameters)
This project was inspired by work by a former Ph.D student at Carleton, Dusan Gostimirovic
  An Open-Source Artificial Neural Network Model for Polarization-Insensitive Silicon-on-Insulator Subwavelength Grating Couplers

## Slide 3: Grating Coupler Parameters
Grating Coupler
  Fiber Angle “Theta” ([])
  Pitch ([m])
  Duty Cycle (Unitless)
  Fill Factor (Unitless)
Light
  Mode (TE/TM)
  Wavelength ([m])

## Slide 4: Methodology
Generating simulation data from Lumerical and properly formatting it for processing
  Manually generating the simulation data
  Generating the simulation data by a script
Develop, train, test and validate a neural network
  Investigate different hyperparameters
  Optimizers for training

## Slide 5: Job Distribution
Data Generation
  Deng Mading
  Randi Wan
ANN Development
  Jonathan Levine
  Jacob Ryall

## Slide 6: Lumerical Data Generation (Script Method)
By – Yu Wan (Randi)

## Slide 7: Outline
Introduction
FDTD Settings
Challenge
Innovation
Future Plan

## Slide 8: Introduction
Data Generation
Carleton Remote Desktop
FDTD LUMERICAL
What I used?
What I did?
How I did?

## Slide 9: FDTD Settings

## Slide 10: SOI Subwavelength Grating Coupler
[1]
5 Parameters
  Fibre Angle
  Pitch
  Duty Cycle
  SWG Fill Factor
  Modes
    TE
    TM
3 Materials
  Optical Fibre
    Core
    Cladding
  Oxide
  Substrate

## Slide 11: Material Settings
Core
Cladding
Oxide
Substrate
  n = 1.44
  n = 1.43482
  SiO2
  Si

## Slide 12: Simulation Settings
Mesh Setting
  Auto non-uniform
Port 2
  TM Mode
Port 3
  TE Mode
Wavelength Range
  1.3 – 1.7 µm

## Slide 13: Verify the Setting
[1]
Fibre Angle = 14.375°
Pitch = 0.75 µm
Duty Cycle = 0.65
Fill Factor = 0.25
T_(TE) = 0.34
λ_ (TE) = 1.61 µm
T_(TM) = -0.32
λ_ (TM) = 1.591 µm

## Slide 14: Challenges

## Slide 15: Challenges
Unfamiliar with the Software
Enormous Amount of Data
Undesired Format
Time Consumption

## Slide 16: Innovation

## Slide 17: Coding Method
Setting Parameters
Iterating Parameters
Record Results
  8^4 = 4096 simulations
  Fibre Angle (5 °- 20 °)
  Pitch (0.5 µm – 1.5 µm)
  Duty Cycle (0.4 – 0.8)
  Fill Factor (0.2 – 0.6)
  Write it to file
  Txt Format

## Slide 18: Advantages
Desired Format
Automatic
Low Risk

## Slide 19: Results

## Slide 20
Verify the Result From ANN
Measure the Energy Consumption
Future Plan

## Slide 21: Q&A

## Slide 22: Reference
[1] D.Gostimirovic and W.N.Ye, ”An Open-Source Artificial Neural Network Model for Polarization-Insensitive Silicon-on-Insulator Subwavelength Grating Couplers,” IEEE JOURNAL OF SELECTED TOPICS IN QUANTUM ELECTRONICS, VOL, 25, NO.3, MAY/JUNE 2019.

## Slide 23: ANN Development
General Computer Specs
  CPU: 6700k @ 4.0 GHz
  Memory: 64 GB (DDR4) @ 2400 MHz
Develop new Grating Coupler models with the PyTorch ML Framework
  Previously this was done in MATLAB
Improve the training approach
  Manual changes to learning rate -> automated setting of learning rate
Figure 1: Supercomputer

## Slide 24: Challenges
New to SOI devices and so figuring out if data was good was a challenge
Getting our models to converge
  Python Pandas default data precision
  Learning rate
  Weight decay
How to handle large datasets with respect to training
  Batching
  Training Time

## Slide 25: Method – Training and Testing Sets
Training Set: 11202 Examples with 200 Transmission Spectra (2,240,400 rows)
  Combination of (n=6) and (n=8) datasets
Testing Set: 512 Examples with 200 Transmission Spectra (102,400 rows)
  Comprised of the (n=3) dataset
Batched the Training set at 10k rows per batch
Held the learning rate at 0.001 for entire training cycle
Figure 2: Training Set
Figure 3: Testing Set

## Slide 26: Results – Training Time
Three Hidden Layers
  Input: (6, 50) -> 50, 50, 100 -> Output(100, 1)
  Training Time: 119.5 mins
Four Hidden Layers
  Input: (6, 50) -> 50, 100, 250, 100, 50-> Output: (50, 1)
  Training Time: 207.6 mins
Five Hidden Layers
  Input: (6, 100) -> 100, 250, 500, 250, 100, 50-> Output: (50, 1)
  Training Time: 298.2 mins
Figure 2: Training Time For Different Network Sizes

## Slide 27: Results - Training and Testing Losses
Figure 4: Losses For 5-Hidden Layer Network
Figure 3: Losses For All Three Networks

## Slide 28: Validation Results – Example 1
Parameters:
Fiber Angle: 14.375
Pitch: 0.75x10^(-6)
Duty Cycle: 0.65
Fill Factor: 0.25
ANN Inference time: 20.25 seconds
Lumerical Simulation time: 130 seconds
Figure 5: TE Mode
Figure 6: TM Mode

## Slide 29: Optimized Results at 1.55 m
ANN Found The Following Parameters (0.4715):
Fiber Angle: 10
Pitch: 1.5x10^(-6)
Duty Cycle: 0.44
Fill Factor: 0.55
Figure 6: TE Mode
Figure 7: TM Mode

## Slide 30: Validation Results – Example 2
Parameters:
Fiber Angle: 5
Pitch: 0.7x10^(-6)
Duty Cycle: 0.48
Fill Factor: 0.2
ANN Inference time: 20.25 seconds
Lumerical Simulation time: 130 seconds
Figure 7: TE Mode
Figure 8: TM Mode

## Slide 31: Future Work
Iterative approach to training the models and generating new simulation data based on training results
Automated Hyperparameter Tuning
Removing noise from the dataset

## Slide 32: Reference:
INTELIGENCIA ARTIFICIAL timeline | Timetoast timelines
NT govt earmarks funds for facial recognition system | Computerworld
Premium Vector | Human face (freepik.com)
D.Gostimirovic and W.N.Ye, ”An Open-Source Artificial Neural Network Model for Polarization-Insensitive Silicon-on-Insulator Subwavelength Grating Couplers,” IEEE JOURNAL OF SELECTED TOPICS IN QUANTUM ELECTRONICS, VOL, 25, NO.3, MAY/JUNE 2019.

## Slide 33
https://www.google.com/search?q=time+is+money+graphic&rlz=1C1GEWG_enCA972CA972&sxsrf=APq-WBuYoK-T9Ro-8MzwZpOi_G0e6oHSVw:1647895128262&source=lnms&tbm=isch&sa=X&ved=2ahUKEwjFivzdh9j2AhWLj4kEHewMD9oQ_AUoAXoECAEQAw&biw=1278&bih=1287&dpr=1#imgrc=LWTSkRfllJl9iM
https://m.researching.cn/articles/OJc2ecdbdc7da0bab2/figureandtable
https://www.ringcentral.com/us/en/blog/effective-teamwork/
https://www.hpcwire.com/off-the-wire/kit-supercomputer-among-the-15-fastest-in-europe/